## Slide 1: Flip angle and Saturation of NMV Saturation Effects of flip angle on saturation and weighting TR and saturation
V.G.Wimalasena
Principal
School of Radiography

## Slide 2: Saturation
In MR pulse sequences, saturation is a nonequilibrium state with no net magnetization. The same amount of nuclear spins is aligned against and with the magnetic field.
So those nuclei will not induce a signal in the receiver coil
In practice this is used in different pulse sequences to manipulate tissue contrast in images.

## Slide 3: Saturation & T1
B0
First RF pulse
Transverse plane
B0
Transverse plane
Relaxation
Water
Fat
Fat
Water
Transverse plane
2nd and succeeding RF pulse
B0
B0
Transverse plane
Partial saturation
Un saturated
Saturated

## Slide 4: Flip angle & Saturation?
The NMV flips with the application of RF pulse
The intensity of RF excitation signal determines the degree of flip angle
Repetition of RF pulses at selected times can produce saturation
When the NMV is pushed beyond 900 it is said to be partially saturated.
When the NMV is pushed to a full 1800 it is said to be fully saturated (or inverted).

## Slide 5: Saturation & weighting
The degree of saturation affects the image weighting
If partial saturation of the fat and water vectors occurs T1 weighting results.
If partial saturation does not occur proton density weighting occurs.

## Slide 6: TR and saturation
Before application of RF pulse the fat and water vectors are align with B0. When the first 900 pulse is applied, the two vectors are flipped into the transverse plane.
The RF pulse is then removed , and the vectors begin to relax and return to B0.
Fat has shorter T1 than water, and therefore returns to B0 faster than water.
If the TR is shorter than the T1 of the tissues, the next (and all succeeding) RF pulse, flips the vectors beyond 900 and into the partial saturation because their recovery was incomplete.

## Slide 7
The fat and water vectors are saturated to different degrees because they were at different points of recovery before 900 flip.
The transverse component of magnetization for each vector is therefore different.
The transverse component of fat is greater than that of water because its longitudinal component grows to a greater degree before the next RF pulse is applied, and so more longitudinal magnetization is available to be flipped into the transverse plane.
The fat vector therefore generates a higher signal than water (fat is bright and water is dark).
A T1 weighted image results. (next slide)

## Slide 8: Saturation & T1
B0
First RF pulse
Transverse plane
B0
Transverse plane
Relaxation
Water
Fat
Fat
Water
Transverse plane
2nd and succeeding RF pulse
Water
Fat
B0
B0
Transverse plane

## Slide 9: Result of No saturation
If the TR is longer than the T1 of the tissues, both fat and water fully recover before the next (and all succeeding) RF pulses are applied.
Both vectors are flipped directly into the transverse plane and are never saturated.
The magnitude of the transverse component of magnetization for fat and water depends only on their individual proton densities, rather than the rate of recovery of their longitudinal components.
Tissues with a high proton density are bright, whereas tissues with a low proton density are dark. A proton density weighted image results. (next slide)

## Slide 10: No saturation & Proton density
B0
B0
B0
B0
First RF pulse
Second & succeeding RF pulse
Fat & Water relax to B0
Transverse plane
Transverse plane
Fat & water in Transverse plane
Fat & Water vectors represent proton density
Unsaturated

## Slide 11: Magnetic Inhomogeneities
These are areas within the magnetic field that do not exactly match the external magnetic field strength.
Some areas have a magnetic field strength slightly less than the main magnetic field, whereas other areas have a magnetic field strength slightly more than the main magnetic field.
Imaging area
B0
B0-ab
B0+ab

## Slide 12: T2* Decay
T2* decay is the increased rate of decay of the FID following the RF excitation pulse when magnetic field inhomogeneities are present.
When the RF excitation pulse is removed, the relaxation and decay processes occur immediately. This decay is faster than T2 decay since it is a combination of two effects.
  T2 decay itself
  Dephasing due to magnetic inhomogenities

## Slide 13
The nuclei in an area of inhomogeneity with a higher field strength have a higher precessional frequency. And, the nuclei in an area of lower field strength, have a lower precessional frequency .
This relative acceleration and deceleration causes immediate dephasing of the NMV. This dephasing is predominantly responsible for T2* decay. This is an exponential process.
In phase
Dephasing
Dephased
Fast
slow
Signal
T2*
Time

## Slide 14: Next
Spin echo pulse sequence